## Slide 1: Tapping & Threading
Mechanical Workshop
Module 7

## Slide 2: Warm – Up
VIDEO

## Slide 3: Objectives
Explain the tapping process.
Explain the threading process.
Differentiate between thread classes
Identify the tap types.
Explain the tapping and threading procedure.
Use the tapping and threading tools to create a tap and a thread.

## Slide 4: Introduction
One of the most effective ways to fasten two or more components is through the use of screws or bolts, secured in properly threaded holes.
This method of fastening is more robust then other fastening methods, allowing repeated assembly and dismantling via simple screwing and unscrewing of the screw.

## Slide 5: Tapping
Tapping is the process of producing threads in a metal using certain tools.

## Slide 6: Threading
A thread is a spiral or helical ridge found on nuts and bolts.
Thread is specified by the diameter and the pitch (number of threads per millimeter)

## Slide 7: Hand Threading Safety
Chips produced by hand threading are sharp and should be cleaned by using a brush or piece of cloth.
Do not use compressed air to remove the metal chips.
Newly-cut external threads are very sharp. Again use a brush or cloth to clean them.
Wash your hands after using cutting fluids or oils.
Have cuts treated by a qualified person.
Be sure the die is clamped firmly in the die stock. If not, it can fall from the holder and cause injury.
Broken tap have very sharp edges and are very dangerous. An extra care should be taken in dealing with broken taps.
VIDEO

## Slide 8: Threads Standards
There are many types of threads used in different applications.
The most frequently used standard is the ISO standard shown below.
Metric | Size | Pitch | Tolerance
M | 6 | 0.75 | 5g

## Slide 9: An example of ISO metric tolerance

## Slide 10: Internal Threading
Internal threads are made with a tool called tap.
The tap is made of carbon steel or high-speed steel (HSS) and are carefully heat-treated for long life.
Taps are quite brittle and are easily broken if not handled properly

## Slide 11: Tap Types
A set of standard hand taps is made of a taper, plug and bottoming tapers
A: Taper for starting thread.
B: Plug tap for continuing thread after taper tap has cut into hole
C: Bottoming for continuing threads to bottom of a blind hole.

## Slide 12: Tap Types
Threads are started with a taper tap.
Then the plug tap is used after the taper tap has cut threads as far into the hole as possible.
Finally threads are cut to the bottom of a blind hole (one that does not go through the part) with a bottoming tap. It is necessary to use the full set of taps, only when a blind hole is to be made.
A: Open or through hole. B: Blind hole that is drilled deeper than desired threads
C: Blind hole with threads tapped to bottom

## Slide 13: Tap Drill
The drill used to make the hole prior to tapping is called a tap drill.
Theoretically, it should be equal in diameter to the minor diameter of the screw that will be fitted into the tapped hole.

## Slide 14
Normal size (mm) | Tap Drill (mm)
M3 x 0.5 | 2.50
M4 x 0.7 | 3.30
M5 x 0.8 | 4.20
M6 x 1.0 | 5.00
M8 x 1.25 | 6.70
M10 x 1.5 | 8.50
M12 x 1.75 | 10.20
Tap Drill
The table below shoes the relationship between the thread normal size (diameter) and the its proper tap drill diameter. {Metric Sizes}
Tap Drill = Normal size – thread pitch

## Slide 15: Tap Wrenches
Two types of tap wrenches are available.
The selection of tap wrench depends on the tap size.
A T-handle tap wrench is used with all small taps while the Hand Tap Wrench is used with large taps.

## Slide 16: Care in Tapping
Use the correct size tap drill
Use a sharp tap and apply sufficient quantities of cutting fluids.
Start the taper tap square with the work.
Do not force the tap to cut.
Avoid running a tap to the bottom of a blind hole and continuing to apply pressure.
Remove burrs on a tapped hole with a smooth file.

## Slide 17: Practical Task
Refer back to the drill gauge project to perform the required tapping and threading. The following procedures have to be followed to complete this task
Select the correct taps and tap wrench
Apply suitable cutting fluid to the tap
Place tap in hole as vertically as possible
Press downward on wrench, applying equal pressure on both handles
If tap is not entered squarely, remove from hole and restart it by applying pressure in direction from which tap leans
Turn tap clockwise one-quarter turn, and turn it backward about ½ turn to break the chip (must turn with steady motion)
Care must be taken not to tap too deep for a blind hole
When finished, clean hole and check with thread gage or appropriate bolt

## Slide 19: Check these websites for more info 
http://www.stanford.edu/group/prl/prl_site/Content/Machine_Shop/Tapping_and_Threading.html
http://www.emachineshop.com/machine-shop/Tap-and-Thread/page580.html
http://www.nmri.go.jp/eng/khirata/metalwork/basic/bolt/index_e.html
http://www.kanabco.com/vms/cutting_tools_tap/cutting_tools_tap_00.html